## Slide 1
School of Engineering
Department of Information Engineering
MSc Degree Course in Robotic and Automation Engineering
Professor:
Sergio Saponara
Tutor:
Federico Rossi
Student:
Giacomo Mugnaini
Analysis, design and implementation of AI/ML-based techniques for automatic video surveillance and control systems in smart cities

## Slide 2
2
Introduction
In the EUPilot context, an AI-based video processing system represents one of the main use case to test the accelerators developed in the project.
For the purpose of creating an innovative and effective solution that improves current security systems, Leonardo developed an AI-based video surveillance system called Ganimede.

## Slide 3
3
Introduction
AI-based video surveillance systems:
Analyze large volumes of data extrapolating intelligent informations
Increase security sending real-time warnings about unwanted or dangerous situations in different scenarios such as smart cities, airports, harbors or critical infrastructures.
Support the activity of control room operators ensuring a more efficient use of resources.

## Slide 4
4
System Architecture
Basically, Ganimede is composed by a set of surveillance cameras (mounted on drones or placed in strategic points) that send over 10000 video streams to edge computing resources (such as GPU NVIDIA Tesla T4 or GPU NVIDIA A100).
At the edge level, data are processed and, if necessary, sent to the control room.
Video Streams
Edge Resources
Control Room
Terminal Video Alarms (if necessary)
Post-process feedback

## Slide 5
5
The application: Man Down
Among all the tasks that can be performed on Ganimede platform, one of interest is the man down task.
It consists of identifying, tracking and counting people lying on the ground.
The algorithm is made of three main components:
Object Detector: detects objects of interest in the scene
Man Down Classifier: performs a filtering and classifies the remaining objects as man down
Tracking Algorithm: tracks and counts all the man down objects

## Slide 6
6
Object Detector
YOLOv5 (You Only Look Once) is a single-stage object detector developed by Ultralytics and completely implemented using the PyTorch framework.
YOLOv5 [1]
Models are trained on Microsoft COCO (Common Objects in Context) dataset which includes 80 classes such as person, bicycle, car, airplane, dog etc…
Models accuracy is evaluated on COCO validation set using the mean average precision (mAP) metric
Models speed is evaluated using a GPU NVIDIA Tesla V100
[1] https://github.com/ultralytics/yolov5

## Slide 7
7
Object Detector
Differences between YOLOv5 models in terms of accuracy and speed.
YOLOv5

## Slide 8
8
Object Detector
YOLOv5 detection: pre-processing
Input image in HWC format and BGR colors
Image converted in CHW format and RGB colors and resized to 640x640
Image normalized (from 0 – 255 to 0 – 1)
[0.027, … , 0.003]
Image flattened
(1D array of 1228800 elements)
Pre-processing is performed on CPU

## Slide 9
9
Object Detector
YOLOv5 detection: inference
YOLOv5 model forward pass
[0.447, … , 0.573]
Model output
(1D output array of 2142000 elements)
[6.52e+00, ... , 8.88e-03]
Image flattened
(1D tensor of 1228800 elements)
YOLO inference is performed on GPU

## Slide 10
10
Object Detector
YOLOv5 detection: post-processing
Post-processing is performed on CPU
Reshape
[6.52e+00, ... , 8.88e-03]
Model output
(1D output tensor of 2142000 elements)
Non-Maximum Suppression
Each array is composed by:
Bounding box in xyxy form (4 elements)
Probability score (1 element)
Class ID (1 element)
Detections
(N array of 6 components)

## Slide 11
11
Man Down Classifier
The man down classifier works following these steps:
Takes all the detections in output by the object detector
Rescales the bounding boxes to the original image dimension
Converts bounding boxes from xyxy form to xywh form
Discards every predicted bounding box with an aspect ratio lower than a threshold, that is
Overrides the class person with man down
Man Down classifier is performed on CPU

## Slide 12
12
Tracking Algorithm
DeepSORT [2]
N. Wojke, A. Bewley e D. Paulus, «Simple Online and Realtime Tracking with a Deep Association Metric» in 2017 IEEE International Conference on Image Processing (ICIP), Beijing, China, 2017.
[2]
DeepSORT is a computer vision algorithm capable of tracking objects while assigning an ID to each of them.
It is considered as an extension of the SORT (Simple Online and Realtime Tracking) algorithm.
It enhances tracking by introducing a Convolutional Neural Network for re-identifying objects across frames.

## Slide 13
13
Tracking Algorithm
Algorithm main parts:
Estimation
Feature Extraction
Data Association
Tracks Handling
DeepSORT
DeepSORT algorithm is performed on CPU

## Slide 14
14
Tracking Algorithm
DeepSORT Estimation: Kalman Filter
The estimation part is performed by a Kalman Filter.
For the detections, a linear constant velocity model is considered.
Autonomous system:
System state:
State variables:
Bounding box center coordinates (, )
Bounding box height ()
Bounding box aspect ratio ()

## Slide 15
15
Tracking Algorithm
DeepSORT Estimation: Kalman Filter
State transition matrix:
Observation matrix:
Process noise:
Measure noise:

## Slide 16
16
Tracking Algorithm
DeepSORT Estimation: Kalman Filter
Kalman Filter prediction step:
is the innovation term
is the Kalman gain
is the updated state
is the updated covariance matrix
is the predicted state
is the predicted covariance matrix
Kalman Filter correction step:
___________________________________________________________________________

## Slide 17
17
Tracking Algorithm
DeepSORT Feature Extraction
Feature extraction is performed by a CNN trained on a large re-identification dataset.
The feature extractor computes particular vectors called appearance descriptors.

## Slide 18
18
Tracking Algorithm
DeepSORT Data Association
Data association represents the core of the DeepSORT algorithm.
The goal of data association phase is to correctly associate detections to pre-existing tracks.
This is done following two steps:
Applying the Matching Cascade algorithm on the set of tracks and detections.
Applying an Intersection over Union (IoU) matching on the remaining unmatched detections and unmatched tracks.
Both the matching problems are solved using the Hungarian algorithm [3].
H. W. Kuhn, «The Hungarian Method for the Assignment Problem,» Naval Research Logistic Quarterly, vol. 2, n. 1-2, pp. 83-97, 1955.
[3]

## Slide 19
19
Tracking Algorithm
DeepSORT Data Association: Matching Cascade
The generic element of the cost matrix is computed as follows:
Where:
is a weight
is the Mahalanobis distance between the i-th track and the j-th detection
is the cosine distance between i-th track and the j-th detection

## Slide 20
20
Tracking Algorithm
DeepSORT Data Association: Matching Cascade
The squared Mahalanobis distance is defined as follows:
The cosine distance is defined as follows:
Appearance descriptors set
(the dimension of the set is a parameter of the algorithm)
Metric that exploits Kalman Filter estimation

## Slide 21
21
Tracking Algorithm
DeepSORT Data Association: Matching Cascade
In addition to the cost matrix, a gate matrix is computed:
Where:
is a weight
and are determined experimentally

## Slide 22
22
Tracking Algorithm
DeepSORT Data Association: Matching Cascade

## Slide 23
23
Tracking Algorithm
DeepSORT Data Association: IoU Matching
Given two bounding boxes, Intersection over Union (IoU) is defined as the ratio between the intersection area and the union area of the two bounding boxes.
The idea behind the IoU matching is the same as the cascade matching:
A cost matrix is computed where the generic element is the IoU between the i-th track and the j-th detection.
The Hungarian algorithm is used to solve the linear assignment problem.
All the matches that have an IoU less than a threshold () are discarded.

## Slide 24
24
Tracking Algorithm
DeepSORT Track Handling
After the data association part of the algorithm, three cases can occur:
First Case: A track and a detection have been matched
Second Case: A track is unmatched
Third Case: A detection is unmatched

## Slide 25
25
Tracking Algorithm
DeepSORT Track Handling
First Case: If a track and a detection have been matched, a bounding boxes with the track ID is applied.
Second Case: If a track is unmatched, it’s marked as missed and goes in a stack. If such track is not detected for frames is terminated.
Third Case: If a detection is unmatched, is discarded.
After all, the age of each track is incremented.
In addition, an object must be detected a certain number of times before being considered a detection. This promotes the avoidance of false positives.

## Slide 26
26
Experimental Tests
Platforms
Tests has been conducted on several different platforms:
CPU ARM Cortex-A72
CPU Intel i7-10750H
CPU Intel i7-10750H + GPU NVIDIA GeForce GTX 1650 Ti (with TensorRT optimization)
CPU Intel Xeon
CPU Intel Xeon + GPU NVIDIA Tesla T4 (with TensorRT optimization)

## Slide 27
27
Experimental Tests
Library used to get GPU stats: NVIDIA Management Library (NVML)
 | NVIDIA Tesla T4 | NVIDIA GeForce GTX 1650 Ti
CUDA Cores | 2560 | 896
Tensor Cores | 320 | None
Total memory | 15110 MiB | 4096 MiB
Memory utilization with no load | 0 % | 0 %
Temperature with no load | 31.0 0.1 °C | 49.4 3.2 °C
Power consumption with no load | 9.0 0.2 W | 2.4 0.2 W
 | NVIDIA Tesla T4 | NVIDIA GeForce GTX 1650 Ti
CUDA Cores | 2560 | 896
Tensor Cores | 320 | None
Total memory | 15110 MiB | 4096 MiB
Memory utilization with no load | 0 % | 0 %
Temperature with no load |  | 
Power consumption with no load |  | 
NVIDIA GPUs informations

## Slide 28
28
Experimental Tests
Tests has been executed using NVIDIA TensorRT, a software library for high performance deep learning inference on NVIDIA GPUs.
It accelerates inference in several different ways:
Reducing model precision preserving accuracy
Fusing layers and tensors
Selecting best data layers and algorithms for the target GPU platform
Reusing memory for tensors efficiently
Executing multiple input streams in parallel
Optimization Tools: NVIDIA TensorRT

## Slide 29
29
Experimental Tests
Results with GPU NVIDIA GeForce GTX 1650 Ti
Test description:
YOLOv5x weights
OSNet weights
Video of 473 frames
Processing at 6.5 FPS
DeepSORT Parameters:
Speed

## Slide 30
30
Experimental Tests
Results with GPU NVIDIA GeForce GTX 1650 Ti
GPU Temperature
Test description:
YOLOv5x weights
OSNet weights
Video of 473 frames
Processing at 6.5 FPS
DeepSORT Parameters:

## Slide 31
31
Experimental Tests
Results with GPU NVIDIA GeForce GTX 1650 Ti
GPU Power Consumption
Test description:
YOLOv5x weights
OSNet weights
Video of 473 frames
Processing at 6.5 FPS
DeepSORT Parameters:

## Slide 32
32
Experimental Tests
Results with GPU NVIDIA Tesla T4
Speed
Test description:
YOLOv5x weights
OSNet weights
Video of 473 frames
Processing at 11.3 FPS
DeepSORT Parameters:

## Slide 33
33
Experimental Tests
Results with GPU NVIDIA Tesla T4
GPU Temperature
Test description:
YOLOv5x weights
OSNet weights
Video of 473 frames
Processing at 11.3 FPS
DeepSORT Parameters:

## Slide 34
34
Experimental Tests
Results with GPU NVIDIA Tesla T4
GPU Power Consumption
Test description:
YOLOv5x weights
OSNet weights
Video of 473 frames
Processing at 11.3 FPS
DeepSORT Parameters:

## Slide 35
35
Experimental Tests
YOLO (average) inference speed comparison
Platforms:
CPU ARM Cortex-A72
CPU Intel i7-10750H
CPU Intel i7-10750H + GPU NVIDIA GeForce GTX 1650 Ti
CPU Intel Xeon
CPU Intel Xeon + GPU NVIDIA Tesla T4